## Slide 1: Line-Maze Solving Robot
Nolan Wagener & Kyle Chiang

## Slide 2: The Standard Maze Problem
No loops!
Fixed start and end points

## Slide 3: Task: Solve Maze to Visit Destinations
Destinations
Robot Can Start Anywhere
Door

## Slide 4: Two Phase Solution: Mapping and Solving
Mapping
  Robot visits unexplored edges, tells computer about intersections
  Computer tells robot actions to take, generates internal map
Solving
  User tells what destinations it wants visited and what doors are open/closed
  Computer generates optimal path for destinations, sends commands to robot

## Slide 5: Levels of Control
User input
Path-finding
PID
Actuator

## Slide 6: Tools Used
m3pi robot
mbed microcontroller
BlueSMIRF Bluetooth modem
S371 color sensor
Laptop with Bluetooth
Python program for maze solving and communication to robot

## Slide 7: Technical Challenge I: Maze Exploration
Can’t just do left hand on the wall
Main idea of our algorithm: Keep track of vertices that must be visited
  Any new vertex that is visited and has edges we haven’t explored get added to our “must-visit” set
  Use uniform cost search to get to vertices that must be explored
  Whenever all edges of vertex is explored, we remove vertex from set

## Slide 8: Technical Challenge II: Color Sensor
Takes too long to get accurate color reading
If included in PID loop, robot cannot track line
Solution
  Use colored tape that can be differentiated by reflectance sensors
  Break out of PID loop and stop robot before reading color sensor

## Slide 9: Technical Challenge III: Reflectance Sensor
Inaccurate detection of intersections
Incorrectly detect path
  Would cause robot to veer off the map
Neglect to detect path
  Incorrect detection during exploration leads to unexplored edges
Solution
  Careful tweaking of thresholds

## Slide 10: Summary
Robot can solve maze with loops
Code can create optimal paths, even under changing conditions
Future Work
  Resolve timing issues
  Optimize PID loop to increase sampling rate

## Slide 11: Questions?